## Slide 2: The beautiful physics of spin qubits:
17.01.2025 | David Divincenzo
But are they a technology?

## Slide 3: Outline
100 years ago – extra 2-level systems in nature
Spin & quantum tunneling
First spin qubit concepts
Surprising path of experiments
Difficulties slowly overcome
Latest concepts
Route to scalability?

## Slide 4
Wolfgang Pauli:
Wissenschaftlicher Briefwechsel mit
Bohr, Einstein, Heisenberg U.a.: Band 1
“classically not-describable two-valuedness”
Spin was the first,
but not the only
example
Notes: Spin naively is “around the axis”
Pauli knew it doesn’t make sense

## Slide 5
Second use of “classically not describable two-valuedness”

## Slide 6
D. D. Awschalom, J. F. Smyth, G. Grinstein, D. P. DiVincenzo, and D. Loss, “Macroscopic quantum tunneling in magnetic proteins,” Phys. Rev. Lett. 68, 3092 (1992); 71, 4276(E) (1993).
My personal first “qubit”:

## Slide 7: NMR quantum computer – 7 qubit operation
Liquid-state NMR
NMR spin lattices
Linear ion-trap spectroscopy
Neutral-atom optical lattices
Cavity QED + atoms
Linear optics with single photons
Nitrogen vacancies in diamond
Electrons on liquid He
Small Josephson junctions
  “charge” qubits
  “flux” qubits
Spin spectroscopies, impurities in semiconductors
Coupled quantum dots
  Qubits: spin,charge,excitons
  Exchange coupled, cavity coupled
Nuclear spin
=1/2 for
F-19 and C-13
“Factored 15.”
(Can’t factor 221.)
I.e., not scalable.
Taught us the value of precision instruments
Taught us a lot about control techniques
c. 1995:
Notes: dicarbonylcyclopentadienyl (perfluorobutadien-2-yl) iron (C11H5F5O2Fe )

## Slide 8
DiVincenzo, Phys Rev. A 51, 1015 (1995)
Science 270, 255 (1995).
Example: early idea -- nanostructure for control of (nuclear) spin
scanning tip

## Slide 9
“Gearbox quantum computer”. Not realistic. But, was a motivation for two
different directions in quantum computing research…
From DiVincenzo, “Two-bit gates are universal for quantum computing,”
Phys Rev. A 51, 1015 (1995)

## Slide 11
Extrapolating Livermore et al. to a quantum computer (LD 1998):
Based on nonrelativistic ideas
  Spin & orbit are uncoupled, except via particle statistics
  Leads to very low coupling to some parts of the environment
  Symmetry determined spin-spin coupling (Heisenberg)
But, problems with nonrelativistic philosophy:
  Strength of Heiserberg interaction sensitive to environmental electric fields
  For control, invoke (relativistic) magnetic controls
Other decoherence channels not really thought through (hyperfine effects)
Very naïve from the point of view of scalability

## Slide 12: Quantum-dot array proposal
Gate operations with quantum dots (1):
--two-qubit gate:
Use the side gates to move electron positions
horizontally, changing the wavefunction overlap
Pauli exclusion principle produces spin-spin interaction:
Model calculations (Burkard, Loss, DiVincenzo, PRB, 1999)
For small dots (40nm) give J~ 0.1meV, giving a time for the
“square root of swap” of
t ~ 40 psec
NB: interaction is very short ranged, off state is accurately H=0.

## Slide 13: Can we get CNOT with just Heisenberg exchange? i.e., can Q. computing be done completely nonrelativistically?
Conventional answer– NO:
--because Heisenberg interaction has too much symmetry
--it cannot change
S (total angular momentum quantum number)
Sz (z component of total angular momentum)
Correct answer (Berkeley & others) – YES:
--the trick: encode qubits in states of specific angular momentum
quantum numbers, with tensor-power structure
-- examples of these sectors with N spins:
Hilbert space dimension 2(N/4) (singlet, S=0)
Hilbert space dimension 2(N/3) (Sz=+N/6, simultaneous in multiple S sectors)

## Slide 14: Specific scheme to get quantum gates with just Heisenberg exchange:
Most economical coding scheme:
1 qubit = 3 spins:
(i.e., singlet times spin-up)
(triplet on first two
spins)
Because quantum numbers are fixed (S=1/2, Sz=+1/2), all gates on
These logical qubits can be performed using SWAP:
from mrs2002

## Slide 15: Economical coded-gate implementations— results of simulations
By varying interactions times shown,
all 1-qubit gates on coded qubits can be obtained with no more
than 4 exchange operations (if only nearest-neighbor interactions)
or 3 exchange interactions (if interactions between spin 1 and spin 3
are possible)
Focus of R&D at HRL research lab (Malibu) for many years

## Slide 16: CNOT on two coded qubits
-minimal solution
19 interactions,
doable in 13 time steps
-essentially unique
-gate accuracy ~10-5
with precision shown
-nearest-neighbor
seems best

## Slide 17: Simple features of scheme for coded computation
--Initialization: turn on uniform B field and strong antiferromagnetic
Heisenberg exchange between spins 1 and 2. Then
is the ground state of the system.
--Measurement: coded qubit is measured by determining whether
spins 1 and 2 are in a relative singlet or triplet. Somewhat easier
than single-spin measurements.

## Slide 18
(1,1)
(0,1)
(1,0)
(0,0)
d)
-400
-415
V2 (mV)
-400
-415
V2 (mV)
V6 (mV)
-530
-520
(0,1)
(1,1)
(0,2)
(1,2)
V =25 mV
2
P
DV
-400
-450
b)
-5
0
5
(0,0)
(0,1)
(0,2)
(1,1)
(1,0)
(1,2)
dGS/dV6 (a.u.)
-500
-550
V6 (mV)
(2,1)
(2,0)
(2,2)
V2 (mV)
t=10 ms
a)
c)
1
8
2
3
4
5
6
9
10
11
12
0.5 mm
GS
-20 dB
V
P
2
7
-20 dB
V
P
6
Details of Charlie Marcus group structures and measurements
-- full electric circuit, measurement by spin-charge conversion
-- charging honeycomb, termination at empty dots
c. 2005

## Slide 19: Two-electron spin qubits, c. 2012
GaAs
Al0.3Ga0.7As
Si doping
+ + + + + + + + + + + +
-
+
Electrostatic gates
Individual confined electrons
GaAs heterostructure
90 nm
2D electron gas
Thanks to Hendrik Bluhm, RWTH
Lengthy efforts to mitigate hyperfine effects (Ga & As nuclei)
Gradual realization: Si and Ge are better (many spin-zero nuclei)

## Slide 20
300nm
Present developments:
  Much improved spin qubits with Si/Ge
  >99% gate fidelities (not 99.9%)
  Multiqubit structures are working (~16)
  Boast: “million qubits on a chip”
    Very misguided – not scalable!
2024

## Slide 21
Partial solution for scalability problem:
  Electron shuttle:
    Move single electron in gated structure by several microns
    OK state fidelity now achieved
    Leads to Infineon/ARQUE scalable architecture
    Problem: extra valley quantum number

## Slide 22
300nm
New development:
  Several problems solved by going to holes
  Different heterostructure, primarily Ge
Veldhorst Scappucci

## Slide 23
Completely different from Loss/DiVincenzo paradigm, highly relativistic:
  Holes, as described by Luttinger Hamiltonian, have complex anisotropy
  g factor structure
    gzz>>2
    gxx, gyy ~ 0
    Principal axes slightly rotated

## Slide 24
300nm
Completely different from Loss/DiVincenzo paradigm, highly relativistic
  Holes, as described by Luttinger Hamiltonian, have complex anisotropy
  g factor structure
    gzz>>2
    gxx, gyy ~ 0
    Principle axes slightly rotated
  But, successful gates by LD mechanism:
  Hole transferred to dot with rotated principle axes, causes Bloch-vector rotation
  Excellent fidelity achieved

## Slide 25
Prospective architecture:
Cold control circuits
Very few cables into cryostat
my skepticism:
  Power consumption
  minaturization

## Slide 26: Observations
Spin qubits: “moderate success”
Explores many interesting physics ideas
Problems of excessive decoherence, extra degrees of freedom slowly overcome
Novel discussions of scaling route, many problems can be foreseen
Revived modern attention to beautiful aspects (e.g., Kohn-Luttinger picture) of semiconductor physics

## Slide 28: Quantum-dot array proposal

## Slide 29: Five criteria for physical implementation of a quantum computer
Well defined extendible qubit array -stable memory
Preparable in the “000…” state
Long decoherence time (>104 operation time)
Universal set of gate operations
Single-quantum measurements
D. P. DiVincenzo, in Mesoscopic Electron Transport, eds. Sohn, Kowenhoven, Schoen (Kluwer 1997), p. 657, cond-mat/9612126; “The Physical Implementation of Quantum Computation,” Fort. der Physik 48, 771 (2000), quant-ph/0002077.

## Slide 30: 5. Measurement requirement
Ideal quantum measurement for quantum computing:
For the selected qubit:
if its state is |0, the classical outcome is always “0”
if its state is |1, the classical outcome is always “1”
(100% quantum efficiency)
If quantum efficiency is not perfect but still large (50%), desired measurement is achieved by “copying” (using cNOT gates) qubit into several others and measuring all.
If q.e. is very low, quantum computing can still be accomplished using ensemble technique (cf. bulk NMR)
Fast measurements (10-4 of decoherence time) permit easier error correction, but are not necessary

## Slide 31
Loss & DiVincenzo
quant-ph/9701055

## Slide 32
Quantum Dot weakly coupled to leads
in the Coulomb blockade regime,
in the presence of a magnetic field B
Spin-polarized current Is
vs. leakage current Ic:
>>1 !
Quantum Dot as Spin Filter and Spin Read-out

## Slide 33
Quantum dot attached to spin-polarized leads*
P. Recher, E.V. Sukhorukov, D. Loss, Phys. Rev. Lett. 85, 1962 (2000)
Spin Read-out via Spin Polarized Leads
* - magnetic semiconductors [R. Fiederling et al., Nature 402, 787 (1999); Y. Ohno et al., Nature 402, 790 (1999)]
- Quantum Hall Edge states [M. Ciorga et al., PRB 61, R16315 (2000)],
Thus: Is = 0
spin up ( Ic << Is )
Is > 0
spin down
=> single-spin memory device, US patent PCT/GB00/03416

## Slide 34: 4. Universal Set of Quantum Gates
Quantum algorithms are specified as sequences of unitary transformations U1,U2, U3, each acting on a small number of qubits
Each U is generated by a time-dependent Hamiltonian:
Different Hamiltonians are needed to generate the desired quantum gates:
1-bit gate
many different “repertoires” possible
integrated strength of H should be very precise, 1 part in 10-4,
from current understanding of error correction
(but, see topological quantum computing (Kitaev, 1997))

## Slide 35: Making the CNOT from exchange:
Exchange generates the
“SWAP” operation:
More useful is the “square root of swap”,
=
Using SWAP:

CNOT

## Slide 36: Quantum-dot array proposal
Gate operations with quantum dots (2):
--one-qubit gate:
Desired Hamiltonian is:
One approach: use back gate to move electron
vertically. Wavefunction overlap with magnetic
or high g-factor layers produces desired Hamiltonian.
If Beff= 1T, t ~160 psec
If Beff= 1mT, t ~ 160 nsec

## Slide 37: Institute for Scientific Interchange, Torino, 1993

## Slide 38: Institute for Scientific Interchange, Torino, 1994
Notes: Need photo

## Slide 43
Foster’s theorem (1924)
Only a theorem for
lossless response!

## Slide 44
Ernst Guillemin with Norbert Wiener

## Slide 45
The solution to the problem of general, exact lossy synthesis came in this work:

## Slide 46
Brune algorithm:
After “Foster preamble”:

## Slide 47
Brune’s fixup:
< 0 !
> 0
> 0
n
Brune’s observation:

## Slide 48
Foster’s theorem, with loss

## Slide 50
1966

## Slide 51
Bernard D. H. Tellegen
Phillips Research

## Slide 54
arXiv:1205.1910

## Slide 55
s1, s2, s3 are the states of the three qubits (0,1)
χi is dispersive shift parameter
Dispersive coupling is the same for each qubit
and the same on both resonators (a and b)
χ=g2/Δ

## Slide 56
Wave impedance
“looking into” port A
(transmission line theory)
Reflection coefficient of full structure
NB
(Z0=50Ω)

## Slide 57
arg(r(ω)) for different qubit states
θ is the same for all even states (mod 2π)
θ is the same for all odd states (mod 2π)
θeven≠θodd

## Slide 58
Alternative solution of Mabuchi and coworkers