## Slide 1
Role of Robotics and Controls in Self-Driving Laboratories
AI-proposed plan needs physical realization
Anuj Tiwari
Chandramouli P Early Career Chair
Assistant Professor
Mechanical Engineering IIT Madras
Email: anujt@iitm.ac.in
1 / 23
Notes: Framing: the modelling side of materials discovery has outrun the physical side. This talk is about the physical side.

## Slide 2
Outline
2 / 23
Where robotics/controls is situated in a self-driving lab
the closed loop with the physical layer
What robotic/controls tasks are present in a self-driving lab
five representative type of tasks based on existing literature
Which technical challenges are there in executing such tasks.
  perception, fragile contact, error recovery, human contact, multi-robot mobility
Notes: Roughly 5 minutes on part 1, 6 on part 2, 8 on part 3, 1 to close.

## Slide 3
The bottleneck
3 / 23
Generative models now propose candidate materials far faster than anyone can make them. The rate-limiting step has moved downstream.
What is cheap(er)
Enumerating candidate compositions
Screening with a surrogate model (once the model is trained)
Proposing a synthesis route
What is expensive
Physically making (synthesizing) the sample
Measuring it (characterization) without human hands
Doing both, unattended (for weeks?)
A self-driving laboratory only accelerates discovery if the physical half of the loop closes reliably. That is also a robotics and controls problem.
Notes: The key reframing of the whole talk.

## Slide 4
The closed loop
4 / 23
The planner provides a reference, not a parameter vector: ramp rate, dwell, flow, dispense force. The robot has to execute it, and the controller has to make that execution repeatable.

## Slide 5
Where robotics can contribute
5 / 23
Throughput. Continuous, unattended operation. A 500-run campaign can become a weekend rather than a semester.
Reproducibility — Machine learning on experimental data is limited by noise, and much of that noise is human. When the same arm grinds the same powder with the same force every time, the variance that remains is chemistry. Robotic execution is what makes the dataset learnable, not just larger.
A formal action space. Once a synthesis must be expressed as machine-executable primitives, a model can search over recipes, not just compositions. That is a prerequisite for autonomous design.
Notes: Emphasise the middle point — audiences under-rate reproducibility as the real product of automation.

## Slide 6
What controls contributes: a hierarchy of loops
6 / 23
Five loops, seven orders of magnitude in period. Most published work optimises the slowest loop.
Most deployment failures happen in the middle three.
Increasing feedback loop time period

## Slide 7
Task 1 — Mobility and transport
An example work cell – to identify type of robotic tasks
7 / 23
Sulaiman, S., Jensen, T.B., Bengtson, S.H. et al. Kinematic analysis and integration of vision algorithms for a mobile manipulator employed inside a self-driving laboratory. Int J Intell Robot Appl 10, 584–600 (2026). https://doi.org/10.1007/s41315-025-00518-3

## Slide 8
Task 1 — Mobility and transport
8 / 23
What the robot should do
Navigate between workstations
Dock with millimetre repeatability
Carry fragile or hazardous payloads
Control content
Omni-wheel base kinematics, holonomic
DH model and inverse kinematics for a 6-DOF arm on a moving base
Workspace analysis to avoid singular configurations before planning
Reported performance
Tracking accuracy | 98.4 %
Grasping success | 96.7 %
Pose estimation error | ±0.53 cm
Detection latency | 71 ms
A UR5e on a Ridgeback omni-directional base, with LiDAR and three RGB-D cameras, inside a working electrolyte / ECMS cell. (Evaluated for a book tracking/grasping task)
Sulaiman, S., Jensen, T.B., Bengtson, S.H. et al. Kinematic analysis and integration of vision algorithms for a mobile manipulator employed inside a self-driving laboratory. Int J Intell Robot Appl 10, 584–600 (2026). https://doi.org/10.1007/s41315-025-00518-3

## Slide 9
7 / 23
Stations are fixed; samples, substrates and consumables move. Interaction happens in the transfers between stations — and in the corridor that robots share with people.
Task 1 — Mobility and transport
An example work cell – to identify type of robotic tasks

## Slide 10
Task 2 — Substrate handling and exchange
9 / 23
Without automated substrate handling and exchange, a human must reload the substrate stack, and the pipeline stops being fully autonomous.
A misplacement here cascades: misaligned deposition, then potentially incorrect characterisation.
Source: Fontenot et al., arXiv:2512.06038 (2025).

## Slide 11
Tasks 3 and 4 — Dispensing, insertion, instrument tending
10 / 23
Precision dispensing and insertion
Milligram-scale solid dispensing with a dual-arm manipulator
Syringe injection into a gas chromatograph, with visual servoing
Contact-rich: force, not just position
Instrument tending
Loading and unloading XRD, ECMS, microscopes, spectrometers
Operating instruments designed for human hands — lids, latches, doors
Reading instrument state through a screen, not an API
Source: Jiang et al., Digital Discovery 2, 1733 (2023); Angelopoulos et al., IROS 2023.

## Slide 12
The four general robotic tasks in a self driving lab
12 / 23
Task | Dominant sensing | Tolerance | Loop period
Mobility, transport | LiDAR, RGB-D | ~1 cm | 0.1–1 s
Substrate exchange | RGB, structured light | < 2 mm, < 2° | 0.1–1 s
Dispensing, insertion | force / torque, vision | mg, sub-mm | 1–100 ms
Instrument tending | vision, proprioception | mm | seconds
No single controller, sensor suite or planning method covers this table. This heterogeneity is itself one of the challenges.

## Slide 13
Challenge 1 — Perceiving objects that have no features
13 / 23
Laboratories are full of glass, and detectors such as YOLO and SAM degrade badly on it: edges dissolve in ambient light, reflections mislead, refraction distorts. Existing transparent-object work targets curved glassware, whose distortion is itself a cue. A flat slide offers no such cue.

## Slide 14
Challenge 1 — Why one detector is not enough
14 / 23
A geometric model catches gross misplacement (> 5.4°, > 5.6 mm) and nothing else.
Below roughly 1.7° and 2.4 mm it fails on every case.
A small CNN on the illuminated edge catches all of them, at 97–100 % confidence.
Fusing both, and declaring success only on agreement, biases the system toward false negatives — the safe direction.
Source: Fontenot et al., arXiv:2512.06038, Fig. 7.

## Slide 15
Challenge 2 — Manipulating things that break (deformable objects)
15 / 23
Side grasping needs stiffness for positioning and compliance for contact.
Those conflict in a single material.
The reported answer is mechanical, not algorithmic: rigid shank, deformable tips, four contact points.
Compliance can be achieved in the controller (such as admittance controller) or in the mechanism.
Choosing where is a design decision.

## Slide 16
Challenge 3 — Detecting and recovering from failure
16 / 23
98.5 % first-time placement over 130 trials is good. It is also not good enough on its own — at that rate a 500-step campaign fails about seven times.
Unattended operation is possible because both failures were detected and automatically corrected.
However, many laboratory failures are irreversible. A dropped crucible or a contaminated reagent is not a reset-and-retry situation.
Imitation-trained policies mimic successful demonstrations, so they cannot recover from execution drift and errors compound — the argument for interactive, RL-trained recovery rather than more demonstrations.

## Slide 17
Challenge 4 — Sharing the workspace with people
17 / 23
A self-driving lab is not a cage: humans intervene, reload, inspect and occasionally push the arm out of the way. An admittance law makes the manipulator a virtual mass–spring–damper — it yields proportionally to an applied force, then returns to its planned trajectory.
S. Sulaiman, T. Jensen, F. Schetter, S. Bøgh, “Admittance-based motion planning with vision-guided initialization for robotic manipulators in self-driving laboratories,” arXiv:2602.07005, 2026.

## Slide 18
Challenge 4 — Compliance has a measurable cost
18 / 23
Stable to 18 N of applied force.
Operator effort falls by 34–38 %.
But maximum trajectory deviation triples and settling time nearly doubles once real sensor noise and mechanical tolerance enter.
Compliance and trajectory fidelity trade against each other. Tuning that trade-off is the engineering.
S. Sulaiman, T. Jensen, F. Schetter, S. Bøgh, “Admittance-based motion planning with vision-guided initialization for robotic manipulators in self-driving laboratories,” arXiv:2602.07005, 2026.

## Slide 19
Challenge 5 — Multi-robot coordination and shared mobility
19 / 23
Two robots, one instrument, one corridor, one human: job-shop scheduling with mobile resources, safety constraints and stochastic task durations.
The schedule must be repaired online every time a task overruns or a recovery fires.

## Slide 20
Challenge 6 — Generalisation
20 / 23
Everything is custom designed
Change the substrate size and you redesign the dispenser, reprint the fingers, and retrain the detector on new data.
Controllers tuned for one material–process window rarely transfer to another.
Cost matters too: a capable arm plus gripper is roughly Rs 30 lakh before any integration — a real barrier to replication.

## Slide 21
Where the difficulty actually sits
21 / 23
Error recovery and generalisation are hard across almost every task.
Perception and fragile contact control concentrate on substrate handling and dispensing.
Multi-robot coordination is a mobility and instrument-tending problem.

## Slide 22
Summary
22 / 23
Robotics can lead to increased throughput in self driving labs, but another important product is reproducibility, which is what makes the resulting data learnable by the outer loop AI/ML algorithms to retrain and update.
The binding constraints today are perception of featureless objects, fragile contact (deformable object manipulation), recovery under irreversibility, safe human contact, and coordination in shared space.

## Slide 23
My research deals with some of the problems
22 / 23
Flexible Object Manipulation Using Industrial Robots
U.S. Patent 11,435,742.

## Slide 24
Learning complex manipulation tasks from human demonstration.
Demonstration
My research deals with some of the problems
Notes: Say the title and thank committee members

## Slide 25
Learning complex manipulation tasks from human demonstration.
Demonstration
Learned Behavior with Similar Goal
My research deals with some of the problems
Notes: Say the title and thank committee members

## Slide 26
Learning complex manipulation tasks from human demonstration.
Demonstration
Learned Behavior with Similar Goal
Learned Behavior with Different Goal
My research deals with some of the problems
Notes: Say the title and thank committee members

## Slide 27
My research deals with some of the problems
22 / 23
Task stage estimation and error detection with recovery in occluded assembly tasks

## Slide 28
References
23 / 23
K. Fontenot, A. Gorti, I. Goel, T. Buonassisi, A. E. Siemenn, “Closed-loop robotic manipulation of transparent substrates for self-driving laboratories using deep learning micro-error correction,” arXiv:2512.06038, 2025.
S. Sulaiman, T. Jensen, F. Schetter, S. Bøgh, “Admittance-based motion planning with vision-guided initialization for robotic manipulators in self-driving laboratories,” arXiv:2602.07005, 2026.
S. Sulaiman, T. B. Jensen, S. H. Bengtson, S. Bøgh, “Kinematic analysis and integration of vision algorithms for a mobile manipulator employed inside a self-driving laboratory,” Int. J. Intell. Robot. Appl., arXiv:2510.19081, 2025.
M. Abolhasani, E. Kumacheva, “The rise of self-driving labs in chemical and materials sciences,” Nature Synthesis 2, 483, 2023.
Y. Jiang et al., “Autonomous biomimetic solid dispensing using a dual-arm robotic manipulator,” Digital Discovery 2, 1733, 2023.
J. Zhou et al., “A multi-robot–multi-task scheduling system for autonomous chemistry laboratories,” Digital Discovery 4, 636, 2025.
A. G. Kusne et al., “On-the-fly closed-loop materials discovery via Bayesian active learning,” Nature Communications 11, 5966, 2020.
L. Pithan et al., “Closing the loop: autonomous experiments enabled by machine-learning-based online data analysis in synchrotron beamline environments,” J. Synchrotron Rad., 2023.
Anuj Tiwari anujt@iitm.ac.in
Thank you.